## Slide 1: Advanced Control for Robotics Surface Treatment
Tasks & Milestones
Motivation & Background
Progress Results
Objectives
Apply, demonstrate, and evaluate compliance force control and iterative learning control (ILC) for deep rolling or burnishing processes using an industrial robot equipped with a roller end effector and force/torque sensor.
Project Deliverables & CDIP
Identification algorithm of robot dynamics (including joint compliance)
Robot dynamics simulation tool with contact dynamics, robot joint compliance, robot motion and force control
Co-simulation tool for combined robot motion and contact dynamics
Run-by-run Iterative motion update algorithm to improve motion/force control and microstructure objectives
Conclusion & Applicability
Development of integrated robot dynamics and FEA simulation for motion and force control of the deep rolling process
Development of iterative learning algorithm for hybrid motion/force control
Demonstration of applicability of hybrid motion/force control and iterative learning control to the deep rolling process
Approach extensible to other robot contact tasks: polishing, grinding, deburring
ARM-19-01-F03
Abhijit Chakraborty, chakraa@utrc.utc.com, 860-610-7761
United Technology Research Center, Rensselaer Polytechnic Institute
5/1/19-4/30/20
Deep Rolling:
Workpiece surface exposed to high local mechanical load using a spherical or cylindrical type tool to induce work hardening and compressive residual stress
Altering mechanical behavior of material, enhancing stability of near-surface structure, reducing peak-to-peak value of surface roughness.
Robotic Deep Rolling
Compared with CNC: lower cost, higher throughput, process flexibility for parts
Large industrial robots: heavy loads, while eliminating work-envelope and motion constraints: hard-to-reach spots like corners, square-bottomed areas, and complex curvatures.
Smooth transition of forces around different geometries or segments of the part: challenging for CNC machines
Task 1: Requirement Development (M1-M3)
- Fatigue life requirement
- Robot accuracy requirement
Task 2: Motion and Force control for Deep Rolling (M1-M5)
- Co-simulation development: ABB dynamics + UTRC FEA
- Hybrid motion/force control algorithm development
- Iterative refinement: ILC
Task 3: Development of Closed-Loop Robotic Deep Rolling Cell (M5-M8)
- RPI Testbed
- UTRC Testbed
Metrics:
Normal force: mean and stdev of normal force error
Robot tool path: mean and stdev of path tracking error
Product quality (material properties)
Cycle time
Performance Evaluation
Baseline: Existing UTRC off-line toolpath generation
Post-treatment material properties:
microstructure (surface roughness,
deformation, residue stress), fatigue
Task 4: Experimental Tests and Evaluations (M8-M10)
- Baseline case studies
- Closed loop case studies
Task 5: Project Evaluation and Reporting (M10-M12)
Iterative Learning Control
R
O
d
FEA
Rolling on flat coupon for roller selection
Construction of simplified surface deformation model for motion/force control simulation
Testbed
Testing on Baxter
Testing on RobotStudio (1D Spring Surface)